### SERVICE BULLETIN

ENGINE DIES

##### NO. 1

DATE:  03/18/1997

#### RE:  ALL 5    Horsepower Briggs & Stratton Industrial Plus Powered Go-Devils

ALL 5.5 Horsepower Briggs & Stratton Vanguard Powered Go-Devils

ALL 9    Horsepower Briggs & Stratton Vanguard Powered Go-Devils

ALL 5.5 Horsepower Honda Powered Go-Devils

ALL 6.5 Horsepower Honda Powered Go-Devils

ALL 9    Horsepower Honda Powered Go-Devils

ALL 20  Horsepower Honda Powered Go-Devils

ALL 24  Horsepower Honda Powered Go-Devils

PROBLEM:  Engine will shut off during operation for no apparent reason.

CONDITION FOUND:  Low-Oil Shut-Off Sensor is shutting off the engine.

SOLUTION:  Add more oil to the engine.

We have had several Go-Devil owner’s call us with the above referenced problem.  The problem is that the Low-Oil sensor is very sensitive for this application.  During the operation of the Go-Devil, the engine is tilted more that it would be for most uses of these engines.  Therefore, the sensor will shut-down the engine at times.  We have found that the best solution to the problem is to add more oil to the engine, just enough so that the oil sensor will not shut off the engine.

If you have any questions about this, please feel free to call us.  We will be more than happy to help you and answer any questions you may have.

# Text boxes

GO-DEVIL( MANUFACTURERS OF LOUISIANA, INC.

18649 Womack Road  (  Baton Rouge, La  70817

(225) 752-0167  (  Fax (225) 752-0175

www.godevil.com