##### SERVICE BULLETIN

BLOWN HEAD GASKETS

###### NO. 10

###### DATE:  06/22/06

RE:  BLOWN HEAD GASKET-23 HP VANGUARD

PROBLEM:  Engine running on one cylinder

CONDITION FOUND:  Head gasket is blown when engine is operated under high temperature and/or high load conditions.

SOLUTION:  If blown head gasket is encountered, replace with new gasket p/n 842622.  It is recommended that both head gaskets (cylinder #1 and #2) be replaced at the same time.  The new gasket design offers improved durability in high load applications.