### SERVICE BULLETIN

#### HANDLE HITS SEAT

##### NO. 4

DATE:  03/26/97

RE:  ALL GO-DEVIL MODELS

PROBLEM:  Tiller handle on Go-Devil hits rear seat when attempting to raise propeller to neutral position.

CONDITION FOUND:  Rear seat in boat is either too high or too far to the rear of the boat to operate the Go-Devil properly.

SOLUTION:  Remove standard tiller handle and install current model handle. If this does not correct problem handle may have to be cut and modified to customers boat.

# Text boxes

GO-DEVIL( MANUFACTURERS OF LOUISIANA, INC.

18649 Womack Road  (  Baton Rouge, La  70817

(225) 752-0167  (  Fax (225) 752-0175

www.godevil.com