### SERVICE BULLETIN

#### LUBRICATOR MAINTENANCE

##### NO. 5A

DATE:  02/28/06

RE:  CLEANING THE PRESSURE LUBRICATOR

We recommend cleaning the pressure lubricator on your Go-Devil yearly. To disassemble the lubricator, unscrew the top one-quarter turn to remove the top and spring. Next pump grease into the shaft housing on the Go-Devil to push the piston out. Wipe the piston and plastic housing thoroughly with a paper towel. If necessary, use soap and water. DO NOT USE A PETROLEUM SOLVENT such as gasoline, varsol, kerosene, thinner or carburetor cleaner. These solvents will destroy these components! After cleaning install the piston and stretch the spring a little to give it a little more tension. Insert the spring and align the cap and screw on one-quarter turn. Pump grease into the shaft housing to fill the lubricator to ¾ full.

# Text boxes

GO-DEVIL( MANUFACTURERS OF LOUISIANA, INC.

18649 Womack Road  (  Baton Rouge, La  70817

(225) 752-0167  (  Fax (225) 752-0175

www.godevil.com