##### SERVICE BULLETIN

HARD STARTING IN COLD WEATHER

###### NO. 8

###### DATE:  10/10/02

RE:  ALL GO-DEVIL MODELS

If a customer has trouble with an engine starting in cold weather, we recommend switching to a lighter weight grease such as Aqua Lube #1.  A #1 grease, by definition, is a grease that has more oil in it.  All new Go-Devils are now filled with Aqua Lube #1 at the manufacturer.  If a lighter grease is not available or extremely cold conditions are making an engine with #1 grease hard to start, the customer can lighten the grease by doing the following:

*Remove Lubricator

*Using a grease gun, pump motor oil into the shaft        expelling grease until oil comes out of the lubricator hole.

*Re-install lubricator

*Run engine to mix oil with grease

In addition, we recommend that customers running engines in cold conditions switch to a synthetic motor oil.