### SERVICE BULLETIN

THROTTLE FREEZING SURFACE DRIVE

#### NO. SD1

DATE:  07/30/2007

RE:  All surface drive engines

PROBLEM:  Throttle cable freezing and will not operate in freezing temperatures.

CONDITION FOUND:   Moisture has entered cable.

SOLUTION:  Raise handle to vertical position.  Using a hypodermic syringe, inject some antifreeze down the side of the inner throttle cable.  This will prevent the cable from freezing.

# Text boxes

GO-DEVIL( MANUFACTURERS OF LOUISIANA, INC.

18649 Womack Road  (  Baton Rouge, La  70817

(225) 752-0167  (  Fax (225) 752-0175

www.godevil.com